## Slide 1
12
SUMMARY
Conclusions & Contributions
Pre-Event
S8 is the behavioural trigger (not S1/S3)
Mina (no S8): midday speeds elevated; Yagiasha: dip
Pre-S8 congestion surge: −0.010 at 13:00
System-wide last-minute rush (commute, not shopping)
During Event
S8 triggers rapid network clearance (+0.045 in 5h)
Peak deviation +0.046 at S10 morning
Speed polarization: 33% clearly faster, 11% slower
~20% roads disappear at S10 peak
Motorways/trunks most affected; local streets mixed
Post-Event
Recovery within ~100 min of All Clear
No post-typhoon rebound congestion
Recovery is demand-driven (not supply-constrained)
Consistent pattern across all 3 typhoons
Contributions
First empirical evidence that Signal 8 (not S1/S3) is the behavioural tipping point for pre-typhoon mobility
500m grid regression framework linking road performance to urban structure
Three-phase (pre/during/post) resilience analysis with per-slot granularity
Limitations & Future Work
Data gaps (Sep 22) limit pre-S1 analysis for some typhoons
Grid-level adj-R² ~0.19: substantial unexplained variance remains
TomTom data excludes zero-traffic roads → survivorship bias
Future: traffic flow volume data, incident integration, causal identification
Conclusions | Pre-during-post resilience framework | Empirical evidence from Hong Kong